GigE Vision® Validation Framework

Zip file contains:

- GeValidationFrameworkSetup.msi

- Setup.exe

- These instructions

You can install the Validation Framework on a Windows based PC as follows:

- If you have a previous version installed, it is recommended to uninstall it first

- Install WinPcap

  - You can download it from http://www.winpcap.org/

- Unzip the content of GeValidationFramework_2013-08-20.zip

- Run setup.exe to install the framework

You can run the Validation Framework as follows:

- Make sure your network card  is configured with a 169.254.1.1 IP address and 255.255.0.0 subnet mask

- From the Start menu in GigE Vision Validation Suite, run TestPluginRunner

- Click choose DLL and select GeValidationFramework_2012-10-25.dll

- Optionally select a test subset with the Browse button

- Connect your device directly to the network card (not through a switch)

- Click the Run button

  - Select the device you want to validate

  - Select where the XML file should be retrieved from – device or hard drive

  - Select where the test report will be saved

If you get errors

  - Run each test on its own to determine the test that fails

  - Some errors are pretty explicit from the tool’s output

  - Capture and review a network trace using Wireshark

  - Fix your device or report a possible issue with the validation code

Notes:

- The GigE Vision Validation Framework must be run as administrator under Windows 7

- Kaspersky's anti-virus should be disabled if running on the PC executing the validation framework

- Some Realtek PCIe GBE Family Controller drivers advertise a maximum transmission unit greater than what the NIC can actually support. In this case, incoming packets are truncated to the actual maximum transmission unit size. If the Validation Framework reports issues and it runs over Realtek PCIe GBE Family Controller, please make sure that the MTU set in the driver is actually supported by the NIC.